Mopar Performance (Advertised Duration. Not @ 50’’)

Looking at the data of the Magnum 7.2 litres for 1970, I have extracted the

following data:

67 4 bbl                            69 SP

Intake           268º                                268º

Exhaust         286º                                284º

Overlap         54º                                    --

Intake lift       0.45 in                            0.45 in

Exhaust lift     0.465 in                          0.458 in

power           375 bhp 4600 rpm          390 bhp 4700 rpm

torque           480 lb/ft at 3200 rpm      490 lb/ft at 3200 rpm.

c/ratio            10.1:1                            10.5:1

pistons           cast                                forged

As I told upper, looking at the performance increase that the six packs and

forged pistons give, it's not worth the effort, so I was looking instead for

cast pistons with a 10,1:1 c/r and the SP camshaft, readily available (in

fact I have bought one) that it's almost the same as the magnum 4 bbl

camshafts.

Mopar Performance Cams (Hydraulic) @ 50’’

ydraulic)

Hughes Cams (Full Power)

Lift                                                Duration

| INT .506" EXH .524" | INT .539" EXH .558" | 223° 228° | 111° | 3.5° BTC 48° BBC | 39.5° ABC 0° BTC |
| --- | --- | --- | --- | --- | --- |

Hughes Muscle car

| HMC 2323 BL | INT .504" EXH .504" | 223° 223° | 108° | 7.5° BTC 43.5° BBC | 35.5° ABC -0.5° ATC |
| --- | --- | --- | --- | --- | --- |

Edelbrock Performer (@ 50’’)

Lift                                                           Duration (degrees)

Inlet                     Exhaust                                   Inlet                Exhaust

.420                        .442                                        204                    214

Edelbrock Performer RPM (@ 50’’)

Lift                                                           Duration (degrees)

Inlet                     Exhaust                                   Inlet                Exhaust

.480                      .495                                             238                 246