Jensen Interceptor lll - Wiper Delay –Complex Style

# Text boxes

(

(

(

(

(

(

(

# Washer Pump

### WLG

### ULG

### RLG

### NLG

LGB

(

(

(

(

(

# Wiper Motor

# Park Switch Connector

Lucas Type 16W or 29W

16W Part No: 54071674A

# Windscreen Washer & Wiper Switch

Lucas: 39366E 3972

Run a new 8-wire loom from the dashboard wiper switch to the centre console. Mount the Hella Wiper delay by removing the car’s “fader” control. These days most modern Radio’s have the “fader” (fore/aft speaker balance control) built in.

(

(

Note: All black wires shown are original Jensen wiring loom items.

## G

Ignition Switched

Positive feed

#### 53M

#### 53S

30/31

31

15

#### New

Hella Wiper Delay

Part No: 5WA001 871-04

Note: Latest Version has contacts numbered as below

### 30/51

### 30/51

### 30/51

### 30/51

### 87A

### 87A

### 87A

### 87A

### 87

### 87

### 87

### 87

### 86

### 86

### 86

### 86

### 85

### 85

### 85

### 85

Relay

1

Relay

2

Relay

3

Relay

4

(

Vital !

Schottky Diode

Farnell Part No: 260850

UK Tel: 0870-1200-200

+

##### Hella “New” Mod’

The delay unit has both an on/off switch and a variable resistor (R6). A simple modifications needs to be made to the unit.

- Remove switch-clamping nut, unclip and open delay unit.

- Locate the on/off switch and unsolder the leg on the “15” contact side.

- Bend the unsoldered leg away and run a wire through the case to an external male connector. This is now the “New” contact (see wiring diagram below).

- Bridge the previously switched contacts with a new wire, soldering the bridge in place.

- Reassemble the unit.

Modified wiring.

=    Action of external on/off – delay knob.

“New”

15

Bridge

No Change

Notes: Features of the delay installation

Why go to all this trouble? When you have completed this installation you will find that when the Hella delay is switched off, the wipers work just as Jensen intended. When the delay is turned on it will only delay the wipe in the slow position.  If the delay is “preset” to a desired delay, it may be left in that position and the wipers turned on/off in the normal fashion.

Relay 2 & 4 provides an electrical configuration to fool the wiper into thinking that the wiper switch is in the off position and this allows the park feature to operate.

Relay 1 provides a negative only when the switch is in the fast or slow position.

Relay 3 stops the delay from working in fast.

The Diode stops the non-powered motor winding from feeding current to Relay 3.

Copyright: James Barnes, UK 2001. Interceptor lll Convertible 1976 2340/1843

R6

On/Off